## Slide 1
Student Innovation | PS001
ROCTARA
A Wall Climbing
Inspection Robot
Team: 404 ERROR SOLVED
Surya K · Sudesh Pillai · Vickkraman K
Sri Venkateswara College of Engineering
WALL CLIMBING ROBOT
360°
Surface Coverage
RF TX/RX
Control System
ROS
Integration Ready

## Slide 2
Problem Statement
A crisis hiding in plain sight — across India and the world
⚠ REAL-WORLD CRISIS
170 bridge collapses in India (2021–25) → 202 deaths, 441 injuries [Newslaundry, 2025]
Gambhira Bridge, Gujarat (July 2025): collapsed killing 22 — locals had warned of visible cracks for years [Al Jazeera]
2,130 Indian bridges collapsed over 40 years; 10.1% due to material deterioration & cracking [Study, 1977–2017]
Human Risk
Workers risk fatal falls inspecting tall structures, bridges, and industrial tanks. No PPE fully eliminates danger at height.
High Cost
Scaffolding, cranes & rope access are expensive. A single manual inspection can cost ₹5–20 lakhs per session.
Missed Defects
Human inspectors routinely miss hairline cracks until they propagate to structural failure. No standardised digital records.
Delayed Action
In the Gambhira collapse, residents warned of cracks years before. Lack of frequent automated monitoring cost lives.
ASCE Report Card: Only 44.1% of U.S. bridges rated in good condition. India's Indian Bridge Management System lists 30% of culverts and 8% of major bridges in "poor condition".

## Slide 3
Objective
Core goals of Project Roctara
PRIMARY GOAL: Design and build an affordable, RF-controlled wall-climbing robot capable of real-time live-video structural inspection — with future-ready ROS integration for autonomous, industry-grade deployment.
01
Wall Adhesion & Mobility
Achieve stable, multi-surface climbing (concrete, steel, glass) using a hybrid BLDC suction + BO DC wheel drive system.
02
RF TX/RX Control
Control the robot via a dedicated ISM-band frequency-synced transmitter-receiver — no Wi-Fi, no latency, reliable in industrial RF environments.
03
Live Visual Inspection
Stream real-time video from an ESP32-CAM to the operator for immediate crack and defect identification during the inspection run.
04
Environmental Monitoring
Monitor gas levels (MQ6, MQ135), temperature & humidity (DHT11), and spatial proximity (ultrasonic) for safe confined-space operations.
05
Full Surface Coverage
Follow systematic boustrophedon (lawnmower) path planning to guarantee 100% surface scan without gaps or repeated patches.
06
ROS Integration (Industry Ready)
Implement ROS nodes for sensor fusion, path planning, and structured defect reporting — bridging student prototype to industrial pipeline.

## Slide 4
Proposed Solution
Roctara — end-to-end RF-controlled inspection platform
How Roctara Works
Lightweight chassis with BLDC vacuum motor for multi-surface suction and four BO DC motors for wall traversal in any direction.
Controlled entirely via a radio-frequency TX/RX system — frequency-bound at a fixed ISM channel for interference-free, sub-20ms latency wireless operation.
High Quality CAM streams live HD video feed to the operator console for real-time visual crack and defect identification.
ROS nodes handle path planning (coverage algorithm), sensor data fusion, and publish structured defect location messages to a ground station dashboard.
KEY INNOVATIONS
RF TX/RX Controller
Frequency-synced control — no Wi-Fi or Bluetooth. Works reliably in RF-noisy industrial plants, substations, and construction sites.
Live ESP32-CAM Feed
Operator sees the robot's exact view in real-time. Immediate identification of cracks, rust, or corrosion during traversal.
ROS Integration
Industry-standard robotics middleware. Enables autonomous missions, sensor fusion, and scalable fleet management in future builds.
Multi-Surface Grip
Hybrid suction + wheel system works on concrete, glass, steel. Mechanical tether prevents free-fall if suction fails.
Comprehensive Sensing
Gas, temperature, humidity, and ultrasonic data logged at each position — vital for confined space safety compliance.

## Slide 5
System Architecture
Hardware & software layers of Roctara
LAYER 1 — OPERATOR CONTROL
LAYER 2 — ROBOT HARDWARE
LAYER 3 — SENSING & PERCEPTION
LAYER 4 — ROS / SOFTWARE STACK
Operator
(Ground Station)
TX Controller
(ISM Band Radio)
Frequency Bind
& Sync
RX Receiver
(On Robot)
Electronic Ducted Fan Mechanism (EDF)
Electronic Speed Controller (ESC 50A)
N20 High Torque Gear Motors
Li-ion
Battery Pack (4S)
Safety Tether
& Edge Sensor
High Quality Cam
(Live Video Feed)
MQ6 / MQ135
Gas Sensors
DHT11
Temp & Humidity
LiDAR Sensor (yet to be implemented)
LED Array
(Illumination)
ROS Node:
Robot Control
ROS Node:
Sensor Fusion
ROS Node:
Path Planning
ROS Node:
Defect Publisher
Ground Station
Dashboard

## Slide 6
Methodology / How It Works
Step-by-step operational flow
1
Deploy & Bind
Robot placed on the target surface. TX controller and RX receiver are bound at a fixed ISM frequency for a secure, dedicated control link.
2
Surface Adhesion
BLDC vacuum motor creates negative pressure grip. BO DC motors handle directional movement. Edge IR sensor halts motion at boundaries.
3
Path Execution
Operator manually drives or activates ROS coverage planner (boustrophedon path) for systematic 100% surface scan without gaps.
4
Live Sensing
ESP32-CAM (future implementation of High Quality Cam) streams live video. Gas sensors and DHT11 monitor environment. Ultrasonic maintains wall-distance for stable positioning.
5
Operator Inspection
Operator visually identifies cracks, rust, or corrosion from the live feed. Marks are logged with robot pose for coordinate tagging.
6
ROS Fusion & Report
ROS aggregates all sensor data and marked defect positions. Ground station generates a JSON/PDF inspection report with defect map.

## Slide 7
Tools & Technologies
Hardware, software, and frameworks powering Roctara
Hardware Components
High Quality CAM (live video stream)
Electronic Ducted Fan Mechanism (suction grip)
BO DC Motors x4 (locomotion)
N20 High Torque Motor Driver
Hobbywing 50A ESC
Li-ion Battery Pack
Sensing & Peripherals
MQ6 & MQ135 Gas Sensors
DHT11 Temp / Humidity
HC-SR04 Ultrasonic Sensor
IR Edge Sensor (safety halt)
LED Array (illumination)
Wi-Fi ESP8266 (telemetry)
Control System
RF TX/RX Controller (ISM Band)
Fixed Frequency Bind & Sync
Manual + Autonomous modes
Failsafe tether system
Command latency < 20ms
LOS range > 200m
Software & Frameworks
Python (image processing & UI)
OpenCV (frame analysis)
ROS Noetic / Humble
rosserial (ESP32–ROS bridge)
Matplotlib (defect mapping)
JSON/PDF report generation

## Slide 8
Results / Output
What Roctara delivers during and after inspection
15–30 FPS
Live Stream
Live Video Feed
CAM streams real-time footage to the operator dashboard at 15–30 FPS. Operator identifies cracks, rust, and surface anomalies instantly from a safe ground position.
Real-Time
Defect Logging
Operator-Flagged Defects
During inspection, operator flags defect frames. Each flag is timestamped and associated with the robot's current surface coordinates — forming a structured defect log.
5 Streams
Sensor Data
Environmental Data
Gas concentration, temperature, humidity, and proximity data recorded continuously. Critical for confined space safety compliance and post-inspection environmental audit.
100%
Coverage Audit
Defect Map & Report
ROS node compiles all flagged defects, sensor data, and robot path into a coordinate-tagged defect overlay map. Auto-generates a PDF/JSON report for maintenance teams.

## Slide 9
Advantages & Limitations
Honest assessment of the current build
✔ ADVANTAGES
Zero human exposure to dangerous heights — no scaffolding or rope access needed
RF TX/RX control is reliable in RF-noisy industrial and construction environments
Multi-surface capable — concrete, steel, and glass with hybrid suction/wheel system
Live video stream enables real-time operator-driven crack and defect identification
ROS integration makes it deployment-ready in professional industrial pipelines
Low cost — open-source hardware stack; fraction of commercial inspection robot cost
Standardised digital defect records enable trend analysis and proactive maintenance
Compact & portable — can be deployed in minutes without setup infrastructure
⚠ CURRENT LIMITATIONS
Suction effectiveness reduces on very rough or highly porous surfaces
Battery cycle ~45 minutes — swappable packs needed for extended inspections
Manual crack logging depends on operator attentiveness and visibility conditions
Autonomous ROS path planning is in active development — currently semi-manual
Why It Matters
Researchers at Drexel University (2024) note: built environment is aging faster than it can be maintained. India recorded 170 bridge collapses (2021–25) claiming 202 lives — most preceded by visible cracking that went unaddressed. Early, automated detection is not optional; it is life-saving.

## Slide 10
Conclusion
What Roctara achieves
Roctara demonstrates that a student-built, cost-effective wall-climbing robot can match — and surpass — traditional manual inspection methods in safety, reach, and coverage. By combining RF-controlled mobility, live CAM video inspection, multi-sensor environmental monitoring, and ROS middleware, it bridges the gap between a student prototype and an industry-deployable structural inspection platform.
Safety First
Zero human exposure to hazardous heights. Removes the single greatest risk factor in structural inspection.
Live & Accurate
Real-time video eliminates guesswork. Operator sees exactly what the robot sees — from the ground.
Industry Ready
ROS stack and modular architecture positions Roctara for real-world industrial deployment.
Scalable
Modular hardware and ROS design ensures long-term extensibility and future autonomous upgrades.

## Slide 11
Future Scope
Where Roctara goes from here
Onboard Edge AI
Integrate a lightweight CNN model (TFLite Micro on ESP32-S3 or Jetson Nano) for autonomous crack classification directly from the live video feed.
Full ROS Autonomy
Complete SLAM-based navigation enabling Roctara to self-navigate, map, and scan large structures without any operator input.
IP65/67 Weatherproofing
Ruggedised sealed chassis for outdoor use in rain, dust, and extreme temperatures — enabling real-world infrastructure deployment year-round.
Multi-Robot Fleet
ROS multi-robot coordination for simultaneous inspection of large surfaces with a centralised management dashboard.
Predictive Maintenance AI
Longitudinal defect data enables trend modelling — predicting structural failure risk before it becomes critical.
Expanded Use Cases
Solar panel inspection, ship hull monitoring, nuclear reactor vessel assessment, and post-disaster structural triage.

## Slide 12
Questions?
We'd love to hear your thoughts on Roctara
404 ERROR SOLVED
Surya K · Sudesh Pillai · Vickkraman K
Sri Venkateswara College of Engineering
Student Innovation Domain | Problem Statement PS001